## Slide 1: Micropython
Sensemakers Amsterdam
November 2019

## Slide 2: History
Python
  Interpreted procedural and object-oriented language.
  Guido van Rossum (Sara, CWI, US)
  First release 1991. Last released version 3.8, October 2019.
  In 2019 #3 most popular language, below Java and C but above C++.
Micropython
  Python 3.5-ish, re-implemented in C for microcontrollers.
  Damien George (Cambridge)
  First release May 2014. Last release 1.11, May 2919
  Kickstarter campaign introducing the PyBoard.

## Slide 3: Micropython.org
Kickstarter campaign introducing the Pyboard line (STM32)
Micropython open sourced on Github:
  micropython/micropython
  micropython/micropython-lib
Ported to:
  STM32, CC3200, ESP8266, ESP32, Teensy, nRF, PIC-16, PowerPC, ARM, SAMD
  Zephyr
  Javascript, Linux, Windows

## Slide 4: CircuitPython
Clone of Micropython, maintained by Adafruit
Supports only SAMD21, SAMD51 and nRF52840 (Adafruit stuff)
Tracks Micropython releases
Changes to Micropython:
  User Interface
  Boot order/behavior
  Hardware IO API model
https://github.com/adafruit/circuitpython/blob/master/README.rst

## Slide 5: Code – bare Micropython
RAM
Flash
pyc-compiler
Interpreter
File System
bin – load module

## Slide 6: Code – add a built-in library
neopixel.pyc
RAM
Flash
neopixel_write
PC: neopixel.pc
pyc-cross compiler
Interpreter
PC: neopixel_write.c
c-compiler
File System
pyc compiler
bin – load module

## Slide 7: Code – flash to module
neopixel.pyc
RAM
Flash
neopixel_write
Interpreter
File System
pyc-compiler
bin – load module

## Slide 8: Code - Code – add your application
neopixel.pyc
boot.py
main.py
RAM
Flash
neopixel_write
Interpreter
File System
pyc-compiler
bin – load module

## Slide 9: Code –start
boot.pyc
main.pyc
neopixel.pyc
boot.py
main.py
not_used.py
RAM
Flash
neopixel_write
Interpreter
File System
py-compiler
bin – load module

## Slide 10: Code – add your code and start
1- boot.pyc
2- main.pyc
3- neopixel.pyc
boot.py
main.py
not_used.py
RAM
Flash
4- neopixel_write
Interpreter
File System
py-compiler
bin – load module

## Slide 11: Out of the box for ESP
ESP deep sleep
ESP WiFi and sockets
Pins (digital and analog), PWM, pulse
1-wire, ds18x20
Neopixel, APA102
DHTxx
I2C, SPI
RTC, Timers, Delay
Touch (ESP32)

## Slide 12: Python or C?
C-code is linked into interpreter -> full build / flash required -> slow workflow
Py code is in the file system -> compiled on the fly -> fast workflow
Hence, only use C if required for timing and Python for all else.
Run Python code from file system. Optionally add to pre-compiled module if stable, general purpose.
In 8 months use no C-code required (one change in the pipe)
Tons of library code implemented in Python (I2C based mostly)

## Slide 13: ESP architecture
UART
PC
USB-Chip
RTOS + Espressif OS
WiFi

## Slide 14: ESP architecture – SMA Demo board
UART
PC
USB-Chip
RTOS + Espressif OS
WiFi
Display
I2C
DHT11

## Slide 15: SMA Demo board + Arduino
UART
PC
USB-Chip
RTOS + Espressif OS
WiFi
Display
I2C
DHT11
Arduino Abstraction Layer ESP8266
pin() , delay(), …, esp_stuff()
Display Library
DHT11 Library
…..
Your sketch:
setup()
loop()
IDE compiles, links, uploads this on every cycle.

## Slide 16: SMA Demo board + Micropython
UART
PC
USB-Chip
RTOS + Espressif OS
WiFi
Display
I2C
DHT11
Micropython, DHT11 module, pin(), …
(web - REPL direct access)
Flash file system with more Python library modules and Python application code in main.py
Occasional toolchain compile, link, upload at version upgrade, bug fix, …
File manager updates changed files only.
rshell - file manager and terminal

## Slide 17: Start-up sequence
Hard boot:
  ESP RTOS boots and inits
    IO ports in default state
    possibly connecting to WiFi
  ESP RTOS starts MicroPython task
Soft boot:
  MicroPython initializes
  MicroPython runs boot.py
  MicroPython runs main.py (which may never exit)
  MicroPython idles waiting for (web)repl connection

## Slide 18: Terminal
MicroPython
  Reserves UART-0 (or soft UART on USB, not for ESP) for console on 115200 bps
  Built in Python REPL (Read Evaluate Print Loop)
  Also a WebREPL on a websocket (optional, but enabled in Sensemakers set-up)
Connect via rshell, putty, uPyCraft, …
  If MP is not idle (main.pu running), abort with ^c
  rshell and uPyCraft are MP-aware and will abort for you

## Slide 19: Rshell
pip(3) install rshell
Find out port/dev for your MP serial connection
rshell –p <whatever>
  Aborts running program
  Syncs MP clock time on your board
  Get a directory listing for the files on your board
  Goes into command mode

## Slide 20: Rshell 2
Commands: ls, cp, rsync, cat, edit, repl, …
Default is current directory.
Files on your board are in /pyboard
  File to board: cp whatever.py /pyboard
  File from board: cp /pyboard/credentials.py mylocaldir/credentials.py
  Changed files from local dir to board: rsync mylocaldir /pyboard
  Enter repl: repl
  Exit: exit or ^d

## Slide 21: In repl
TAB auto completion
^x exit the repl (remember! Only alternative is a hard-reset)
^c abort running statement
^e enter paste mode
^d leave paste mode or start soft-boot
Up/Down access command history
^r execute command

## Slide 22: In repl
If a command produces a result in repl, the result will be printed automatically.
Try:
  dir()
  uos.listdir('')
In a program you would need to use:
  print(uos.listdir(''))

## Slide 23: Connecting to the world
http://docs.micropython.org/en/latest/
http://docs.micropython.org/en/latest/esp8266/quickref.html
Pins
I2C
DHT
Neopixel
…

## Slide 24: Pin
from machine import Pin
pin_obj = Pin( <nr> [,<direction>], [,<mode] )
Examples:
  p2 = Pin(2, Pin.IN, Pin.PULL_UP) # create input pin on GPIO2 with pull_up
  print(p2.value()) # get value, 0 or 1
  p5 = Pin(5, Pin.OUT, value=1) # set pin high on creation
  P5.value(0) # and then set it low

## Slide 25: I2C
from machine import Pin, I2C
i2c = I2C(scl=Pin(<sclpin>), sda=Pin(<sdapin>) [, freq=<freq>])
Examples:
i2c = I2C( scl=Pin(5), sda=Pin(4), freq=100000 )
i2c.writeto(0x3a, '12’) # write '12' to slave device with address 0x3a
buf = i2c.readfrom(0x3a, 4) # and then read 4 bytes response