## Slide 1: MicroPython
How to use in practice?
Modelled on the ESP8266.

## Slide 2: Why doesn’t it works on some boards?
Two versions for the ESP8266 currently. Flash sizes:
  512 kB (stripped version)
  4 MB (full version)
On the SenseMakers site and default on MicroPython 4 MB is used.
Newer boards (e.g. Wemos D1 mini pro ) have 16 MB flash. Flashing uses auto-detect and finds 16 MB. Using this with a 4 MB binary fails.
Work around: Specify flash_size=4MB while flasing instead of autodetect.

## Slide 3: Source options – using the GitHub sources
Want to use the latest version of the code.
Want to add very low level, Python callable drivers in c(++).
Want to contribute to the open source project.
Want to add pre-compiled Python libraries.
Only supported on Linux on Intel/AMD.
  If you have a Mac: use some VM and run Ubuntu.
  If you have Windows: use WSL (2?) or other VM and run Ubuntu.

## Slide 4: Demo – Add a simple library
In demo.py put:
def hello_sensemakers():
print('Hello SenseMakers, how are you all’)
Add to the appropriate module (../ports/esp8266/modules)
make deploy

## Slide 5: machine
Built-in library with low level i/o stuff
Pin
I2C

## Slide 6: Pin
https://docs.micropython.org/en/latest/library/machine.Pin.html
  Pin numbers are the ESPxx GPIO numbers. Not the fancy numbers your board manufacturer invented.
Examples:
  my_SDA_pin = Pin(4)
  my_SCL_pin = Pin(5)
  my_LED_pin = Pin(12, Pin.OPEN_DRAIN)
  my_switch_pin = Pin(13, Pin.IN, Pin.PULL_UP)
Use:
  my_LED_pin.on()
  my_switch_pin.value()

## Slide 7: Flash a LED on ESP8266
3.3 V, max sink = 20 mA
LED on 10 mA, voltage drop 0.7 V
3.3 – 0.7 = 2.6 V
U = I * R -> R = U / I -> 2.6 / 0.010 = 260 ohm
- Connect +3.3V to 260 ohm to LED to pin 12
my_LED_pin = Pin(12, Pin.OPEN_DRAIN)
my_LED_pin.off()
- Explain

## Slide 8: Flash LED
from time import sleep
while True:
my_LED_pin.value(1- my_LED_pin.value())
sleep(3)

## Slide 9: Machine I2C
from machine import Pin, I2C
my_SDA_pin = Pin(4)
my_SCL_pin = Pin(5)
i2c = I2C(scl=scl, sda=sda)
print(I2c.scan())